| SCT Low-Mass Power Tapes ] |
| --- |
| Abstract |
| This document describes SCT low-mass power tapes, produced on aluminium-Kapton laminates. |
| Prepared by : | Checked by : | Approved by : |
| M. Mikuž, V. Cindro, T. Weidberg |  |  |
| Distribution List |
| Table of Contents |

<!doctype html public "-//w3c//dtd html 4.0 transitional//en">

Low mass power tape specifications

# Requirements

## Modularity

## Length

## High Voltage

## Low Voltage

## Sensing and control

## Additional requirements

# Design

## Basic design considerations

## Tape design

## Tape construction

## Tape properties

## Resistivity and voltage drop

## Material

## Space and routing

## Transmission line properties

1 Requirements

Low-mass aluminium power tapes carry detector bias (HV), power, sensing and control levels in the SCT barrel harness from PPB1-N  to module dogleg. Functionally same tapes run from PPF0 to PPF1 in the end-caps.

1.1 Modularity:

Basic modularity is given by the SCT power distribution philosophy, stating that each module should be served individually. This results in one power tape used for each of the 4088 (2112 barrel & 1976 forward) modules. Tapes are grouped into barrel harnesses where 6 tapes serve one barrel half-stave. Each barrel harness is shielded individually, the shields are connected at PP1. In the forward region 2-3 tapes from each PPF0 are combined en route to 5-6 tapes on  PPF1.

1.2. Length:

The range of tape lengths in the barrel is 0.8 - 1.6 m, in the forward 1.3 - 3.1 m. Length distribution of individual tapes for the barrel is given in Appendix A. It was obtained by A. Nichols from measurements on the UCL barrel mockup.

1.3 High Voltage

According to SCT Bias Voltage Power  Specification V2.03 (draft) :

- Vmax = 500 V (HV component rating)

- Imax = 5 mA

1.4 Low Voltage

According to ATLAS SCT Low Voltage Power  Specification V2.0 (draft)

analog (ABCD bipolar FE):

- Icc,max = 1260 mA

- Icc,nominal = 900 mA

- Vcc,nominal = 3.5 V (( 5 %)

digital (ABCD + opto CMOS)

- Idd,max = 990 mA

- Idd,nominal = 570 mA

- Vdd,nominal = 4.0 V (( 5 %)

PIN bias

- Vmax = 10 V

- Imax = 2 mA

VECSEL drivers

- Vmax = 6.6 V

- Imax = 10 mA

1.5 Sensing and control

Sensing

- temperature on module (2 on barrel, 1 in forward)

- Vcc, Vdd and respective returns at module connector (4 sense lines)

Control

SELECT for clock (opto redundancy scheme)

- Vnominal = 4.0 V

- Imax = 1 mA

RESET module

- Vnominal = 4.0 V

- Imax = 1 mA

All the lines except for the RESET carry DC levels.

1.6 Additional requirements

Maximize conductivity

Rather large currents flow through power tapes into the Inner Detector. The voltage drop requires the voltage at power supplies to exceed the safety limit of the ABCD chip (DMILL process) of 5.5. V. A voltage protection circuit at PP2, using sense wires to monitor and eventually clamp the voltage, will be used. But still, small voltage drop adds to safe operation and allows voltage limiters to function in case of a sense wire malfunction. Power dissipation, a sizable portion of it in the cold SCT volume, is another nuisance from the large currents. So the design should maximize conductivity to:

- minimize voltage drop

- minimize power dissipation

Minimize material in sensitive region

Material in the Inner Detector deteriorates its performance as well as that of the calorimeter. The importance of material grows towards the interaction point. Therefore, the design should:

- minimize radiation length

- minimize interaction length

Minimize space

Space is scarce in the ATLAS Inner Detector. The design with tapes tends to:

- maximize conductor to insulator ratio

- minimize packing factors

Transmission line properties

To avoid noise pick-up by power tapes and its injection into the read-out chips on the module the tape design should

- maximize coupling capacitance

- minimize inductance

Radiation hardness

All materials used in the tape design should be radiation resistant up to radiation levels encountered in the ATLAS SCT:

- 100 kGy ionizing radiation

- 2.x 1014  n/cm2 (1 MeV neutron NIEL equivalent)

2 Design

2.1 Basic design considerations

The tapes are designed as long, but simple, two-layer flexible circuit with conductor/KAPTON laminates.

IPC standards for flexible printed circuits are taken as design guidelines with the caveat that no IPC standards exist for aluminium flexes. Standards for copper flexes are obeyed and appropriate tests carried out where aluminium properties are suspected to pose a risk for flexible tape operation. 0.5 mm track and gap grid is chosen to match 1 mm pitch, 25 mil (0.635 mm) was felt too risky.

2.2 Tape design

The lines are grouped  into:

low current – assigned to minimal 0.5 mm tracks

- HV

- HV_ret

- V_cc_sense

- A_gnd_sense

- V_dd_sense

- D_gnd_sense

- TEMP_1

- TEMP_2 (barrel only)

- PIN_bias

- ILED_a

- ILED_b

- SELECT

- RESET

resulting in 12(13 in barrel) narrow tracks,

and high current – assigned wide tracks

- V_cc

- A_gnd

- V_dd

- D_gnd

yielding 4 wide tracks.

Tracks are grouped in two layers with matching supplies and returns for RF filtering and minimal loops.  IPC-2223 specification is obeyed for HV separation (500 V - 2.5 mm). 50 um Al is taken as conductor,  for its 4 times smaller radiation length than Cu for the same conductivity.  21 mm tape width was compatible with on-barrel engineering constraints

So 9 mm remain for power lines, shared equally between digital and analog supplies. Barrel design  and  forward design are shown in Figs. 1 and 2.

2.2 Tape construction                                                                         index

Basic materials originate from GTS Ltd. (holder of ISO 9001 ). They form a matched product line of:

- Al(Cu)/Kapton FPC laminate with PU glue

- glue

- glue/Kapton coverlayer

The PU glue was tested by CERN-TIS for radiation hardness at the level required, Kapton is specified as radiation hard.

inner part - "thin" low-mass tape

bottom to top

- 25 um Kapton/25 um PU glue/50 um Al laminate (GTS prod. # 660210AL)

- 25 um glue (GTS prod. # 102100)

- 25 um Kapton/25 um PU glue/50 um Al laminate (GTS prod. # 660210AL)

- 25 um glue/12.5 um Kapton coverlayer (GTS prod. # 322190)

outer part - "thick" low-mass tape

bottom to top

- 50 um Kapton/25 um PU glue/70 um Cu laminate (GTS prod. # 760220ED)

- 25 um glue (GTS prod. # 102100)

- 50 um Kapton/25 um PU glue/70 um Cu laminate (GTS prod. # 760220ED)

- 25 um glue/12.5 um Kapton (GTS prod. # 322190)

tape ends chemicaly Ni/Au plated for contact/soldering according to IPC-6013 Class 3

- Ni minimal layer thickness: 1.3 um

- Au maximal layer thickness: 0.8 um

Tape Properties                                                                         index

Resistivity

of 4.5 mm power lines

- 250 mOhm/m round trip (thin)

- 110 mOhm/m round trip (thick)

of 0.5 mm lines

- 2.24 Ohm/m round trip (thin)

- 0.97 Ohm/m round trip (thick)

all values with nominal values for Al and Cu resistivity,

- Al : 2.8 uOhm.cm

- Cu: 1.7 uOhm.cm

GTS sheet resistance spec for Al 2.5 - 2.7 uOhm.cm (?)

view  voltage drop table  for baseline SCT power distribution

Material

input:

- X0(Cu) = 1.43 cm

- X0(Al) = 8.9 cm

- X0(Kapton) = 35 cm; all glues assumed ~kapton

The width of all conductors is

4*4.5 + 13(12)*0.5 = 24.5(24) mm (in brackets forward cables without the TEMP2 line)

X-section of plastic

- thin:   21 mm * (25(K) + 25(G) + 25(G) + 25(K) + 25(G) + 25(G) + 12.5(K)) um = 3.4 x 10-2 cm-2

- thick: 21 mm * (50(K) + 25(G) + 25(G) + 50(K) + 25(G) + 25(G) + 12.5(K)) um = 4.5 x 10-2 cm-2

Radiation length seen at perpendicular impact for one cable (w - width over which the material is spread)

single thin tape 
X1 / X0 = (S/X0  (Al}) + S/X0  ({plastic})) / w = (1.23(1.20) mm2 / 89 mm + 3.4 mm2 / 350 mm) / w =  (0.014 + 0.010) mm / w 
= 0.024 mm / w

single thick tape 
X1 / X0 = (S/X0  (Cu}) + S/X0  ({plastic})) / w = (1.72(1.68) mm2 / 14.3 mm + 3.4 mm2 / 350 mm) / w =  (0.0120(0.118) + 0.010) mm / w 
= 0.130(0.128) mm / w

thin cable

spread over cable  (w = 21 mm) X = 0.114 % X0 spread over module (w = 60 mm) X = 0.040 % X0 end of stave over module (6 cables) X = 0.24 % X0 outer barrel radius (1056 cables, r = 520 mm)  X = 1056 * X1  / (2.pi * r) = 0.78 % X0 (this should be the maximum) at cryostat wall (1056 cables, r = 1150 mm)  X = 1056 * X1  / (2.pi * r) = 0.35 % X0 at end of forward cylinder (988 cables, r = 590 mm)  X = 988 * X1  / (2.pi * r) = 0.64 % X0 (maximum in forward)

Beware of fast conclusions from these numbers ! In the worst case, tapes are traversed twice and at an angle of 35o (barrel) or 13o (forward). 
The worst-case material estimate in thin low-mass tapes seen by particles is therfefore 2.7 % X0  in the barrel and 3.5 % X0  in the forward.

thick cable

spread over cable  (w = 21 mm) X = 0.619(0.610) % X0 spread over cryostat bore (1056 barrel cables, r = 1150 mm) X = 1056 * X1  / (2.pi * r) = 1.90 % X0 on cryostat face (1056 barrel + 988 forward cables, r = 1200 mm) X = (1056 * 0.130 + 988 * 0.128)  / (2.pi * r) = 3.49 % X0 (maximum)

Space and routing

X-sections, nominal thickness (measured somewhat smaller)

- 2.1 * 0.02625 = 0.055 cm2 (thin)

- 2.1 * 0.03525 = 0.074 cm2 (thick)

envelopes, shielding (50 um foil per harness) & packing factors (1.2) not taken into account

minimal bending radius: 10 x tape thickness (IPC-2223 5.2.4.2.)

- rmin = 3. mm (thin)

- rmin = 4. mm (thick)

thin tape (no IPC for Al !) tested: bending over a mandrel (r = 5, 2, 0.75 mm), 100 180o bends, repetition 1 Hz

result:

- r = 5 mm O.K.

- r = 2 mm O.K.

- r = 0.75 mm

- 30 bends  O.K.

- 50 bends  1 broken line

- 100 bends  3 broken lines

Al tape safe, if IPC recommendations followed

Transmission line properties

eps (Kapton) = 3.5 
eps (glue) = eps (Kapton)

capacitance: C / l = eps * eps0 * w / d

- 1.9 nF/m (thin)

- 1.4 nF/m (thick)

inductance: L / l = u0 d / w

- 20. nH/m (thin)

- 28. nH/m (thick)

for comparison: flat (TP) ribbon cables: C/l  typically 50 pF/m, L/l  700 nH/m

Production                                                                         index

Production is with a standard photolithographic process adapted to the size of the circuits.

Mask production

Laminate polishing

Photo-resist lamination

Photo-resist exposure

Photo-resist development

Conductor etching

Photo-resist stripping

Polishing

Ni/Au deposition

Laminate/glue/laminate/coverlay pressing

Tape cutting

Quality control and testing

Production steps are carried out according to production sheets of the producer (available in Slovenian). Quality control actions for separate steps are as follows:

Mask production

Laminate polishing

Photo-resist lamination

Photo-resist exposure

Photo-resist development

Conductor etching

Photo-resist stripping

Polishing

Ni/Au deposition

Laminate/glue/laminate/coverlay pressing

Tape cutting

# Scope of the document

# Introduction