RD42 meeting, March 6-7, 2009
ATLAS BCM (Beam Condition Monitor) and
ATLAS BLM (Beam Loss Monitor) status
Andrej Gorisek, Irena Dolenc
(Jozef Stefan Institute, Ljubljana)
[Speaker Notes: Theme created by Sakari Koivunen and Henrik Omma Released under the LGPL license.]

---
BCM: introduction
8 BCM detector modules around IP to monitor beam conditions close to the IP
by
T. Kittelmann
ATLAS Inner
detector
BCM detector
modules

---
BCM: principle of operation
Time of flight measurement to distinguish between normal collision and	background events (beam gas, halo, TAS scraping) on a bunch-	by-bunch basis
2 detector stations (each with 4 detector modules) at zBCM=1.84m:
particles from collisions reach both stations at the same time  “in time” hits, occurring every bunch crossing
particles from background interactions occurring at |zb|>|zBCM|reach nearest station 12.5 ns before particles from collisions at IP  “out of time” hits
use “out of time” hits to identify the background events
use “in time” hits to monitor luminosity (additional information provided by BCM)
Requirements:
fast and radiation hard detector & electronics:
rise time ~1ns
pulse width ~3ns
baseline restoration ~10ns
ionization dose ~0.5 MGy, 1015particles/cm2 in 10 years
MIP sensitivity
zb

---
BCM: readout chain
PP2
~10Gy
ATLAS counting room USA15
BPSS
~0.5MGy

---
BCM: detector modules
Double – decker assembly
signal passively summed before
amplification
2 back-to-back pCVD diamond sensors
each with
thickness 500μm,
Size: 10×10 mm2
Contact size: 8×8 mm2
Operated at 2V/μm (1000V)
 fast & short signals
Modules titled by 45o towards beam
Front end electronics
2 stage amplifier:
1st stage: Agilent MGA-62653, 500MHz (22db)
2st stage: Mini Circuit GALI-52, 1GHz (20dB)
BCM detector
module
Typical
signal
13.4 cm

---
BCM: modules installed on Pixel Support Structure
Beam
Pipe
BCM
module
Pixel
Detector

---
BCM: NINO board
NINO chip: Time-over-threshold amplifier-discriminator chip
Analogue signal converted into a digital level signal at fixed time after the input signal arrival
Output signal width correlated to the input signal amplitude
To increase the dynamic range: analogue signals split in two channels in ratio of 1:11 before “digitisation”  16 channels (8 low and 8 high attenuation channels)
Channels Module
(high, low atten.) position
0, 8 A +x
1, 9 A +y
2, 10 A -x
3, 11 A -y
4, 12 C +x
5, 13 C +y
6, 14 C -x
7, 15 C -y

---
BCM: Status I
Detector installation: done
Electronics: all chain done (firmware upgrades planned)
DAQ/DCS/DataBase: done (cleanup ongoing)
DQM: histograms filled (needs some attention)
Trigger: 6/9 bits into CTP
Montecarlo description: done
full detector description since Athena 12-00 (bug fixed in 15-00), digitization since 14-X

---
BCM: Status II
Calibration/Other:
Thresholds need to be set-up for all channels on the basis of signal
Status of luminosity determination related effort:
First ideas:
http://indico.cern.ch/getFile.py/access?contribId=0&sessionId=1&resId=0&materialId=slides&confId=17599

---
BCM: Status III
Beam separation (Van der Meer) scans:
Dry run with LHC successful (end of November 2008).
Tested communication between CCC and ACR
BCM “rates”
separation
in mm (from LHC)
RecordDataFlag 1=Data valid
(from LHC)

---
BCM: first results
ID combined cosmic run (December 2008)
Checked BCM data in two ATLAS DAQ trigger streams (TRT, RPC):
Trigger timing plots: BCM hit distribution over 31 bunch buckets (bunch crossing intervals-25ns)
Signal seen in timing plots for both streams
RPC
TRT
Mean=19.2
Sigma=1.7
Mean=19.3
Sigma=0.6
Bunch bucket
Bunch bucket

---
BLM: introduction
6 detector modules (with diamond sensors) on each side of IP, installed on the Inner Detector End Plate (IDEP)
z~3450mm, r~65mm
installed modules measured with SMU
(IVs + long term bias: ATL-IC-TR-0007)

---
BLM: readout
Partially adapted from the LHC BLM developed by AB/BI group
Modules readout by 2 “tunnel cards”: BLMCFC
BLMCFC converts current into frequency and sends encoded data over optical link to the “surface card”: BLMTC
Integration times ranging from 40μs to 84s
BLMTC:
inserted in BCM VME crate
VME bus used for monitoring rates and recording the postmortem buffer
Modified BLMTC FPGA firmware to output beam dump signal on the front panel LEMO outputs

---
BLM: detector module
Mechanical support
rad-hard PEEK plastic support
standard double sided PCB – mechanical rigidity and electrical insulation
layers screwed together with M3 screws
Sensor:
8x8 mm2 0.5 mm pCVD diamond
(by DD Ltd.)
metallised at OSU
operated at 500V
Assembly:
conductive glue, bonding, soldering

---
BLM: status
BLMCFC crates modified and assembled with modified PS module and backplane
BLMTC card will be modified to output beam dump signal on the front panel
Communication between SBC and BLMTC trough USB bridge established
ready to bring back the module for FPGA firmware upgrade to AB/BI
setup in the lab (161 01-023)
BLMCFC
BLMTC
SBC
USB-bridge

---
Summary
BCM
Installed and operational
Seen first signals from cosmic data in December 2008
BLM – ready
Detector modules installed in 2008
All parts of hardware available
BLM – to-do
Install BLMCFC (PP2)
Install all parts of PS and control chain (USA15)
Develop code for monitoring rates (running sums) and acquiring postmortem (beam dump) buffer