## Slide 1: Simulations and detector technologies for the Beam Loss Monitoring system at the ESS linac
Irena Dolenc Kittelmann, Thomas Shea
(ESS)
HB2016, July 3-8, 2016, Malmö, Sweden

## Slide 2: Outline
The ESS linac
The ESS BLM system: detector technologies
Monte Carlo (MC) simulations for the ESS BLM
  Tasks
  SW Tools and ESS linac geometry
  Part of the simulation task in more details.
  Note: here the focus is on the MC simulations for tracking of the lost protons outside the beam pipe in contrast to the beam dynamics simulations for beam optics optimization (the lost protons from those are inputs the MC simulations under discussion)
Summary

## Slide 3: ESS linac
ESS – neutron source based on a proton linac
  Nominal average beam power = 5MW
  Proton energy at the target = 2GeV
  Beam current = 62.5mA (1.1109 p/bunch)
  Beam pulse = 2.86ms
  Repetition rate = 14Hz
Normal conduction linac (NCL):
  LEBT, RFQ, MEBT, DTL (5 tanks)
Superconducting linac (SCL):
  Spoke, Elliptical, Contingency and contingency sections

## Slide 4: ESS BLM: detector technologies
Plan to use 3 types of detectors
ESS SCL– ICBLM (Ionisation Chamber based BLM)
Showers of secondary particles (charged and neutral) are expected in the SC linac.
Parallel plate gas Ionisation Chambers (ICs) developed for the LHC BLM system will be used – chosen due to their fast response.
ICs ordered in Summer 2014 (production line setup in Russia, to replenish spares for LHC and make prod. series for ESS and FAIR).
Inner structure of the LCH BLM [3]
Data from [2], [3]

## Slide 5: ESS BLM: detector technologies
ESS SCL - ICBLM (contd)
Background due to RF cavities must be taken into account when using ICs
  Bckg. mainly due to el. field emission from cavity walls, resulting in bremsstrahlung photons created on cavities/beam pipe materials.
  Levels are difficult to predict numerically – they depend on the quality of cavities.
  Energy spectra estimations: up to tens
  of MeV can be expected [4].
  Plan to asses this experimentally as well
Sensitivity of LHC ICs to photons:
  “cut off” at transversal photon and electron
  Incidence <~2MeV (~30MeV for p and n) [5]
Background sampling and subtraction in the
signal processing needed
ESS SCL - 2nd detector type: - cBLM?
(Cherenkov based BLM)
Currently considering to design Cherenkov radiation sensitive detectors
  to be used as an addition to the ICs as the primary BLM detectors in the SC parts
  Cherenkov radiation based detector: to minimise the sensitivity to the RF cavity background
LHC BLM IC response functions [10]

## Slide 6: ESS BLM: detector technologies
ESS NCL:
Plane to place BLM detectors in MEBT in DTL
DTL: protons (3.6-90MeV) stopped in the 3-5cm stainless steel walls
Expected particle fields
outside of the DTL tanks
dominated by neutrons and
photons.
Same conclusion holds for
MEBT (3.6MeV).
Range of protons in copper and SS316L
(calculations with SIRM [1])

## Slide 7: ESS BLM: detector technologies
ESS NC linac: nBLM (neutron sensitive BLM)
Micromegas detectors will be used in these parts of the linac
Detector (and electronics) design on-going by the micromegas experts from CEA Saclay (French In-kind contribution)
The idea is to design a micromegas detector sensitive to
fast neutrons and “blind” to photons (X- and γ-rays)
based on signal discrimination.
Polyethylene
MM
+
B4C
MM +
Polyethylene + Al
~10 cm
~20 cm
Cd or other absorber
Current proposal: assembly of 2 modules [6]
  1st module (slow losses)
    Capable of monitoring low fluxes (~few n cm-2s-1)
    Polyethylene: moderator to thermalize the incoming fast n
    B4C layer(s) to capture thermalized n
    Cd (~mm) to eliminate background thermal n
  2nd module (fast losses)
    appropriate for high fluxes of n, coming from the front
    Polyethylene for n conversion to p recoils (~ few mm) through n elastic scattering on H atoms.
    Al foil or deposition (~50nm) on the polyethylene (thickness defines the neutron energy threshold), followed by a micromegas
Taken from [6]
Taken from [6]

## Slide 8: ESS BLM simulations: tasks
MC simulations needed to determine:
  System response time limit
  Detector locations
  Dynamic range of the system
  Initial MPS threshold settings at the startup and later adjustments to those - not discussed here
  Anticipated response of the system during fault studies (either to verify the system response or to provide information to the accelerator physics faults studies) – not discussed here
Inputs needed:
  Ideally one would have
    A list of accidental beam loss scenarios with loss maps in connection to the elements that must be protected together with acceptable beam loss levels.
    Expected loss maps during normal operation when lowest signal expected.
  However, simplifications/assumptions are needed, due to too large number of possible accidental scenarios in a linac.
Note: most of the results presented here are focused on the nBLMs due:
  Previous efforts solely focused on SCL - some preliminary estimations already exist
  Anticipated neutron and photon spectra at detector locations required for the in-kind partner to start the detector design

## Slide 9: BLM ESS simulations: SW and linac geometry
Simulation tool:
  Geant 4 (v10.00.03) simulation framework developed by the ESS neutron detector group [8]
  Physics list: QGSP_BIC_HP
  Cuts:
    No tracking cuts set
    Production cuts: for e-,e+ and photons set to 10m; for p set to 0
ESS linac geometry:
  Certain element models (quads, Spoke and elliptical cavities, mid part of the elliptical cryomodules) adapted and changed where needed from existing ESS linac model made for the shielding calculations with [9].
  Magnetic field maps for the SCL quads outside the beam pipe included – has important impact on the simulation results for detectors placed close to the quads [?? Edgar]
  Aperture along the linac follows the values in the 2015 baseline beam physics lattice of the ESS linac (2015.v1 ??)
  Tunnel walls included (important for neutron spectra)
  Current simplifications:
    Simplified quad geometry (yoke and coil extent, also the length the quads in the end parts of the linac has recently changed)
    Simplified model of the DTL gaps (build with 1-2 cylindrical shapes on each side of a gap with fraction (gap distance)/(cell width) fixed for each tank) [?? Renato helped]
    Model for cavities in High Beta sections is calculated by scaling part of the Medium Beta cavity profile
    Not included: postcouplers in DTL, Beam instrumentation, Correctors, supports, MEBT chopper and chopper dump , spoke cavity insertions
    ??

## Slide 10: ESS BLM simulations: linac geometry
DTL “detector” volumes
Spoke Cavity
quad
Medium Beta cavity
DTL tank1
DTL tank5

## Slide 11: Response time
Response time requested by the ESS machine protection group [10] ??:
  In NC linac (MEBT-DTL): ~5 μs.
  In SC linac: ~10 μs.
  Numbers based on a simplified melting time calculations, where a block of material (copper or stainless steel) is hit by a beam of protons with a uniform profile under perpendicular incidence angle, no cooling considered [11].
Numbers recently rechecked with update parameters and Gaussian beam
  NC linac: calculated melting time values
  of 3-4μs imply we should be even faster
  than 5μs (confirmed also with a MC
  imulation)
  SC linac: the 10μs requirement for
  response time fits well with these
  calculations
DTL
MEBT

## Slide 12: Response time
However: melting time depends on the incidence angle, is perpendicular incidence a good assumption?
What is the least shallow incidence angle of the most focused beam that can be expected to hit the aperture?
  Expected to occur for a particular case of incorrect setting for a set of corrector magnets – time consuming beam dynamics simulations required to asses that
  Simplification: (cite Ryoichi ??)
    Find such a deflection from expected initial condition (x,x’,y or y’) at the beginning of the section, which still allows for the beam to enter the section (increasing the difference even more would end in beam hitting the walls of the section)
    Take the highest deflection along this section as the worst case angle.
  Assessment of this type performed for DTL and HEBT
    DTL tank1: peak x’ or y’ ~50mrad
    DTL tank2-3: ~15mrad
    DTL tank4-5: ~10mrad
    HEBT: ~20mrad

## Slide 13: Response time
Implications for the response time:
NC linac:
  Depending on the gap distance, an incidence
    close to perpendicular potentially possible
    in the DTL tank1 due to the almost flat
    surfaces between the gaps
  Only possible for inc. angles above ~150mrad
    (to be verified in more realistic DTL geometry)
    – nevertheless, 150mrad still close to perpendicular incidence (??)
SC linac:
  Plan to check the beam pipe melting time.
  However: experience at SNS already justifies the 10μs response time requirement.
  Degradation of cavities observed at SNS after loosing <15μs pulse of 26mA beam ~10/day [12].

## Slide 14: Detector locations
Most suitable set of detector locations (and count): insures the system is not blind to any accidental loss.
In the absence of the list of accidental losses with loss maps, the following strategy is assumed in order to select detector locations:
  Select a set of localised loss scenarios with selected beam energy, incidence angle and loss location along the linac section under investigation.
  Vary the Incidence angle from ~1mrad up to worst case (see p.12)
  Energy??
  Use phantom detector (vacuum) surround the section and run a simulation for each of the loss scenarios in order to produce hit maps of incoming neutrons (for nBLM NCL) or all particles (for ICBLM in SCL).
  Extract the hit map mean and RMS values along the section length and compare with the origin of the loss
  By comparing of the results from all the sim. runs one can extract the best detector locations
nBLM in NCL: current focus here due to need for our inputs by the In-Kind partner
ICBLM in SCL: similar strategy based on optimisation methods combined with genetic algorithms for selecting the locations has been tried in past [???] – work not completed, plan to finalise this with the above mentioned simplified strategy.

## Slide 15: Detector locations
DTL tank1 example (preliminary): proton beam under 50mrad towards det1
Incoming neutron hit maps for 3 different localised loss locations along the DTL tank1
For both det 1 and det2:
  Mean z values agree with the loss locations to ~0.02 - 0.8m depending on the loss location
  RMS z values ~1.4-1.5m (for both det1 and det2)
Same holds if det. volume placed below the tank (with lowest number of hits)
Possible solution: 2-3 (potentially granulated) 1-2m long detectors along the tank ??
det2 “detector”
volume
x
y
z
det1
det0

## Slide 16: Dynamic range
Dynamic range can be determined once the detector locations are know by inspecting 2 extreme cases:
Highest expected hit rate:
  Marks the “worst case” accidental loss (most focused beam under least shallow angle hitting a detector)
  Assumption: use the angles as discussed on p. 12 as the “worst case” – simulated hit rate (or energy deposition or current) corresponds to the estimated upper limit for the dynamic range
Lowest expected hit rate:
  Typically the dynamic range lower limit is set to a fraction of a 1W/m loss distributed uniformly along the linac - coming from a limit for hands-on maintenance
  However, the system should be integrating the received dose and signal problems if this value reaches the allowed limit.
  Therefore it is important to check what are the expected signals during the normal operation of the linac (lowest expected rates – apart from the case of probe beam) – the dynamic range lower limit can than be set to a fraction of this signal ???

## Slide 17: Dynamic range
Expected loss map during normal operation [?? Yngve]:
Results from a beam dynamics error study performed with Tracewin (on the 2015 baseline beam physics lattice of the ESS linac – 2015.v1) has been used as a an input to the BLM MC simulations.
Errors were applied to 10k machines (600k macroparticles each)
Error tolerance set to 100% of the nominal value – apart for dynamic error (RF jitter), where error tolerance increased to 200%)
DTL
Spoke
MB
HB
HEBT

## Slide 18: Dynamic range
Norm. op. vs. 1W/m loss in NCL
For the NCL: MC simulated normal operation loss and 1W/m loss neutron spectra compared
Normal operation: lost protons in the BLM MC simulation were sampled from the lost particle distribution obtained from he previously mentioned error study:
  No limitation on the statistic of the BLM simulation
  No assumptions on the lost particle distributions
  Correlation observed (and used in sampling) between the azimuth angles for lost proton position and momentum direction
1W/m loss:
  Uniform distribution of lost protons assumed along the linac
  Proton polar angle form the beam axis fixed to 1mrad
  Proton azimuth angle (vertical plane) sampled uniformly around the aperture
  Energy set to the nominal value at the lost proton location
Geometry:
  Sections included: MEBT, DTL1-5, 4 first cryomodules of the Spoke section
  Phantom detectors (vacuum) placed around the tanks (see p15)

## Slide 19: Dynamic range
Norm. op. vs. 1W/m loss neutron spectra (neutrons/s hitting the det. vol.) in SCL
Uniform loss:
Increase in incoming neutrons
with the tank number (neutron
cross section increases with Ek)
Normal operation loss:
Neutron flux lowest in the last two
tanks (emittance decreases with Ek)
Norm. op. vs. 1W/m loss
All spectra for the 1W/m above
the corresponding ones for norm.
op. loss (except for DTL1, det0, where
1W/m loss slightly below nor. op.).
The difference increases with tank
number (~0 to ~1.5 order of mag.)
Norm. op: det1
Norm. op: det0
1W/m: det1
1W/m: det0

## Slide 20: Dynamic range
Dynamic range for nBLMs in NCL parts
  Lower limit: will be set to 10% of the flux expected during normal operation, once detector location and size are set. ???
  Upper limit: to be set by assuming focused beam under “worst case” angle
Dynamic range for the ICBLMs in the SCL parts:
  Preliminary values have been set in the past [13]:
    “BLM is required to be able to measure at least 1% of 1W/m loss during normal. operation and up to 1% of the total beam loss” - gives an estimation on input FE current range 800nA – few mA for the BLMs in SCL.
  Plan to re-assess that once the detector locations are fixed. ???

## Slide 21: Summary
The ESS BLM system is planned to be based on 3 types of detectors:
  Ionisation chambers will be used as the primary detector in the SCL parts (ICBLM)
  Future plans: explore an option to use Cherenkov radiation based detectors, where m as a complementary monitor to the ICBLM in SCL. These
  Neutron sensitive micromegas detecors will be used as BLMs in the NCL parts – detector design is currently ongoing by the micromegas team from CEA Saclay
BLM Monte Carlo simulations:
  In the past all effort connected to simulation focused on the SCL parts.
  However currently the focused turned to the NCL parts due to the need for the in-kind partner’s ned for the inputs in order to design the nBLM detectors.
  Strategies to determine the requirements (???) needed for the design of the system (response time, detector locations, dynamic range) were discussed.
  Some preliminary results for the NCL parts were presented, together with the past results focused on the SCL.

## Slide 22: References
[1] http://www.srim.org/
[2] M. Stockner, “Beam loss calibration studies for High energy proton accelerators”, PhD thesis
[3] M. Hodgson, “Beam loss monitor design investigations for particle accelerators”, PhD thesis
[4] B. Cheymol, “ESS wire scanner conceptual design”, ESS-0020237
[5] M. Stockner et al, “Classification of the LCH BLM ionisations chamber”, Proc. Of DIPAC 2017
[6] T. Papaevangelou, “Micromegas as a beam loss monitor”, ESS BI forum, 10-11 Feb. 2016,
https://indico.esss.lu.se/event/441/contribution/22
[7] E. Donoghue et al, “Studies of electron activities in SNS-type SC RF cavities”, Proc. Of 12th Int. Workshop on RF Supercondictivity, Cornell Univ., USA
[8] T. Kittelmann et al, "Geant4 Based Simulations for Novel Neutron Detector Development” 20th International Conference on Computing in High Energy and Nuclear Physics (CHEP) (2013);
[9] I.Tropin et al, “ESS accelerator prompt radiation shielding design assessment”, ESS-0052477 (??)
[10] A. Nordt, “Beam Instrumentation interfaces to protection systems”, TAC12, ESS, https://indico.esss.lu.se/indico/event/315/session/9/contribution/32/material/2/1.pptx (?? 10us?)
[11] L. Tchelidze, “How Long the ESS Beam Pulse Would Start Melting Steel/Copper Accelerating Components?” ESS/AD/0031, http://docdb01.esss.lu.se/DocDB/0001/000168/001/Time_Response_Requirements_BLM.pdf
[12] W.~Blokland et al, “ A new differential and errant beam current monitor for the SNS accelerator”, IBIC2013 (THAL2), Oxford, UK.
[13] L. Tchelidze et al., “Beam Loss Monitoring at the European Spallation Source”, IBIC2013 (WEPC45), Oxford, UK

## Slide 23: Back up material

## Slide 24: Background photons due to RF cavities
Photon background due to the RF cavities mainly
due to field emission from electrons from cavity
walls, resulting in bremsstrahlung photons
created in the field of nuclei of cavity/beam pipe
materials [7].
Energy spectra estimations show that photons up to few tens of MeV can be expected [5]:
  A MC code (FLUKA) was used for these estimations
  where a pencil electron beam is impacting a 4mm
  niobium foil.
  Purple curves on the plot on the left show expected energy
  spectra for the photons produced at the exit of the foil:
    Solid line – for the monochromatic beam of electrons with energy of 25MeV
    Dotted line – for the beam of electrons with uniform energy distribution
    from 0 to 25MeV.
    Spectra are normalised per number of primaries.
  Note: maximum acc. Gradient expected at ESS ~25MeV/m, cavity size ~1m.
e-
γ

## Slide 25: ESS BLM detector count
NC linac - nBLMs
~1-2 devices per m
MEBT: 1 per collimator or chopper dump (??)
DTL: at least 1/tank, 1 between the tanks, 1 at start or end of the DTL
SC linac - ICBLMs
3-4 devices per doublet lattice cell: 4 where there is a cryomodule and 3 in the transport section.

## Slide 26: Response time
Response time requested by machine protection [10] ??:
  In NC linac (MEBT-DTL): ~5 μs.
  In SC linac: ~10 μs.
  Numbers based on a simplified melting time calculations, where a block of material (copper or stainless steel) is hit by a beam of protons with a uniform profile under perpendicular incidence angle, no cooling considered [11].
Numbers recently rechecked with update parameters and Gaussian beam profile
  SRIM calculations used to extract the highest dE/dx (at the Bragg peak), where highest temperature is reached. This serves as an input to calculated the time needed to reach the melting temperature under constant irradiation.
  For the NC linac recheck with a MC calculation for the worst case (most focused 3.6MeV beam under perpendicular incidence) – melting time values agree (3-4μs)
  NC linac: the calculations imply that we should be even faster than 5μs
  SC linac: the 10μs requirement for response time fits well with these calculations